## Slide 1: Portable Building Applications
WoT Use Case
Gabe Fierro
Colorado School of Mines / NREL
gtfierro@mines.edu https://gtf.fyi

## Slide 2: Increasing Amounts of Data Available for Buildings
Large sensor/actuators networks:
  thousands, 10s of thousands of data streams and control points
  Increasing #s of IoT devices available
Opportunity for wide-scale data-driven analytics and control:
  AFDD
  Virtual metering
  Performance measurement
  Automated regulatory reporting
  MPC and advanced controls/sequence-of-operations
  Demand response
Issue: complex, heterogenous configuration:
  Every building is a unique, one-off collection of “data silos”
  Implementing software, extracting data, defining control surfaces is site-specific, error-prone and time consuming

## Slide 3: ...but that data is increasingly hard to use
“Data-rich but information-poor”
  Plenty of phenomena, but none of the context
Understanding this data is a significant bottleneck
  ~40% of consultant/data-scientist time spent understanding metadata
  Manual, time-consuming, error-prone, expensive task
Costs impede adoption of sustainable practices
  2004 NIST report estimates lack of interop @ $15.8 billion/year
  2016 PNNL report: existing work focuses on connectivity, with data semantics still lacking
  2018 study: 70% of commercial buildings have digital controls, but only 4% have automated fault detection
Notes: “Data-rich but information-poor”
Impedes adoption of data-driven sustainable practices, technologies
  Manual configuration of software; site-specific implementations
  ~40% of consultant/data-scientist time spent understanding metadata
Interoperability costs impede adoption of sustainable practices
  2004 NIST report estimates lack of interop @ $15.8 billion/year
  2016 PNNL report: existing work focuses on connectivity, with data semantics still lacking

## Slide 4
Building Management System (BMS): the “operating system” for your building
Point: a source of data from a cyber-physical system 10s or 100s of thousands of points in a typical system
Notes: Data sequestered in proprietary data silos speaking proprietary protocols

## Slide 5: Deploying Cyber-Physical Applications at Scale
Current Practice: manual, time-consuming, error-prone reimplementation for each site

## Slide 6: Deploying Cyber-Physical Applications at Scale
Goal: Write one implementation, run it everywhere without any* manual configuration

## Slide 7: Architecture of a Self-Adapting Application

## Slide 8: How WoT Fits In
Brick ontology defines the data sources and their context w.r.t. the building subsystem
Assumes the data is already in a regular format
  Outsources the “lifting” to the data ingester
Does not handle the discovery of device capability
  Assumes this is already modeled

## Slide 9: How WoT Fits In
It is not enough to model the capability of a device
  Where* is the device?
  What is it connected to?
  What do its actions affect?
WoT standardizes repr. of/access to the I/O capabilities of the IoT devices providing/receiving data
Abstract over (legacy) industrial control protocols:
  BACnet, OPC, LonTalk, Modbus, ...
WoT helps extract data

## Slide 10: Future Brick Work? (The work we don’t want to do…)
Starting to think about the “network/instrumentation view”:
  How are devices connected; how do they communicate?
  Joel Bender (Cornell, BacPypes, ASHRAE, 223P) working on SHACL representation of BACnet objects
Standard enumerations of device properties:
  Thermostat modes, staged equipment, etc
  Aid in data interpretability
Schedules of operation:
  Investigating schema.org-style schedules; RRULE; etc
  Want to express device behavior in terms of schedules (nighttime setbacks, etc)